Model Predictive Control
# Introduction
This document is a tutorial for the code inside mpc.c at the project CControl.
The document is going to explain the code in three steps. First step is going to explain mathematics. The second step is going to explain the mathematics in MATLAB-code. The third step is going to explain the MATLAB-code in C-code from the mpc.c file.

The mathematics in this document has its origin from the B.Sc thesis “Model Predictive Control for an artificial pancreas” by Matias Sørensen and Simon Kristiansen from Technical University of Denmark, Kongens Lyngby 2007.

The reason why I created this mpc.c file is because I have seen many MPC-projects that are applied inside a laboratory environment such as numerical software simulations or expensive physical hardware. Regardless of which, they are not suitable for low cost devices.

The goal of this document is to distribute the knowledge of practical MPC for low cost devices. This document will explain the pros and cons with MPC compared to PID. The document will also explain the rule of thumbs how to set the parameters.

The MPC algorithm inside this mpc.c contains the following:
Iterative quadratic programming
Integral action
Disturbance input
Constraints on input
Soft constraints on output
Constraints on rate of movement
Regularization
Kalman-Bucy filter

Daniel Mårtensson
Sweden
2025-05-03

# Prerequisites
In order to understand this document. One must know the following:
Arrays, variables, functions and memory allocation with C programming
Matrix multiplication
Vector multiplication
Discrete state space modeling
Numerical integrals by using code
# Main
## Header
There are two files for the MPC. It is the source file mpc.c and the header file mpc.h. Begin to read the header file mpc.h. One should observe the following functions inside code
bool mpc_init(MPC* mpc, const float A[], const float B[], const float C[], const float E[], const float sampleTime_mpc, const float sampleTime_kf, const float qw, const float rv, const float qz, const float s, const float Spsi_spsi, const size_t row_a, const size_t column_b, const size_t row_c, const size_t column_e, const size_t N, const size_t iterations);
void mpc_set_constraints(MPC* mpc, const float umin[], const float umax[], const float zmin[], const float zmax[], const float deltaumin[], const float deltaumax[], const float alpha, const float antiwindup);
STATUS_CODES mpc_optimize(MPC* mpc, float u[], const float r[], const float y[], const float d[], const bool integral_active);
void mpc_estimate(MPC* mpc, const float u[], const float y[], const float d[]);
bool mpc_free(MPC* mpc);

The function mpc_init is the first function you should start with. That function creates all the matrices and computes the kalman-bucy filter gain matrix K etc.

After that function has been called, then it’s time for calling the function mpc_set_constraints for setting the limitations of the system. For example, the input cannot be more than 12-bit (0 to 4095) and the output cannot be warmer than 100 degrees.

The function mpc_optimize shall be placed inside the control loop such as a while loop. It will optimize the input signal that is going to be fed into the control output e.g PWM.

For every control input that has been optimized, then mpc_estimate must be called to estimate the next state x for the MPC.

The function mpc_free is only for deleting all allocated memory of the MPC.

## Source
### mpc_init
#### Discretization of MPC and Kalman-Bucy filter
We begin with the mpc_init function. The first thing that happens is that it needs to turn the time continuous state space model, as described in Equation 1, into a time discrete state space model, as described in Equation 2.

alignl dot x(t) = Ax(t) + Bu(t) + Ed(t) newline alignl y(t) = Cx(t) Equation 1: Time continuous state space model
alignl x(k+1) = bar Ax(k) + bar Bu(k) + bar Ed(k) newline alignl y(k) = Cx(k) Equation 2: Time discrete state space model
MPC works with prediction horizons and therefore it must have a discrete model. The benefit by using MPC is that it can “look” into the future and predict the future control signals. If the sample time of the discrete state space model is Ts = 1 second and the MPC has its prediction horizon e.g N = 5 . That means the MPC is “looking” Ts times N = 5 seconds further into the “future”. The MPC “simulates” the model behavior during control time and computes the suitable input signals. This cannot be achieved using a time continuous state space model because the sample time of time continuous model is Ts = 0 seconds.
The Figure 1 illustrates this MPC algorithm in action where the input is predicted with a control horizon of N = 20 and a discrete model of sample time Ts = 10 .

Figure 1: MPC in action from MataveControl in GNU Octave

##### Mathematics:
To make time continuous to time discrete, use this formula in Equation 3.

left [ matrix{A # B # E ## 0 # I # I} right ] = e^{M times Ts} -> M = left [ matrix{bar A # bar B # bar E ## 0 # 0 # 0} right ] Equation 3: From time continuous to time discrete
Where:
- System matrix: A in Re^{ nx times nx } . Input matrix: B in Re^{ nx times nu } . Output matrix: C in Re^{ nz times nx }
- Disturbance matrix: E in Re^{ nx times nd } . Number of states: nx . Number of inputs: nu
- Number of outputs: nz . Number of disturbances: nd . Sample time: Ts in Re
##### MATLAB code:
The ending d is the label for discrete matrix.
[Ad, Bd, Cd, Ed] = DiscreteMatrices(A, B, C, E, Ts_mpc);
[Adkf, Bdkf, Cdkf, Edkf] = DiscreteMatrices(A, B, C, E, Ts_kf);
##### C code:
mpc->Ad = (float*)malloc(row_a * row_a * sizeof(float));
mpc->Bd = (float*)malloc(row_a * column_b * sizeof(float));
mpc->Cd = (float*)malloc(row_c * row_a * sizeof(float));
mpc->Ed = (float*)malloc(row_a * column_e * sizeof(float));
mpc_discrete_matrices(sampleTime_mpc, A, B, C, E, mpc->Ad, mpc->Bd, mpc->Cd, mpc->Ed, row_a, column_b, row_c, column_e);
The discretization is exactly the same for the Kalman-bucy filter. The only difference is that the sample time for Kalman-Bucy must be equivalent as the real time dynamics of the system. Meanwhile the sample time for MPC should be consider as a tuning parameter. The ending kf is the label for kalman filter.
mpc->Adkf = (float*)malloc(row_a * row_a * sizeof(float));
mpc->Bdkf = (float*)malloc(row_a * column_b * sizeof(float));
mpc->Cdkf = (float*)malloc(row_c * row_a * sizeof(float));
mpc->Edkf = (float*)malloc(row_a * column_e * sizeof(float));
mpc_discrete_matrices(sampleTime_kf, A, B, C, E, mpc->Adkf, mpc->Bdkf, mpc->Cdkf, mpc->Edkf, row_a, column_b, row_c, column_e);
#### Kalman-Bucy gain matrix K
Kalman-Bucy filter is used instead of regular Kalman filter. The reason is that Kalman-Bucy filter computes the kalman gain matrix K from the Algebratic Riccati Equations, meanwhile the regular Kalman filter converges the kalman gain matrix K during runtime, which takes more computational resources. Fun fact: The Kalman-Bucy filter is actully the Kalman filter that was used inside the Apollo program. The Kalman-Bucy filter is used because it’s successor to the original Kalman filter.
##### Mathematics:
In order to find the Kalman-Bucy gain matrix K filter, one most solve the Discrete Algebratic Riccati Equation (DARE) by using an ODE-solver such as Runge-Kutta 4:th order and others. Begin first to replace bar A <- bar A^T and bar B <- bar C^T . Then find the solution P .

P = bar A^T times P times bar A - (A^T times P times bar B ) times ( R + bar B^T times P times bar B )^-1 times ( bar B^T times P times bar A )+ Q Equation 4: Discrete Algebratic Riccati Equation
Once the solution P is found, then compute the kalman gain matrix K form the Linear Quadratic Regulator (LQR) control law.

K = (bar B^T times P times bar B + R)^-1 times (bar B^T times P times bar A) Equation 5: LQR control law
##### MATLAB code:
% Create the kalman gain matrix K
syse = mc.ss(delayc, Adkf, Bdkf, Cdkf);
syse.sampleTime = Ts_kf;
Qw = qw * eye(nx);
Rv = rv * eye(nz);
[K] = mc.lqe(syse, Qw, Rv);
##### C code:
mpc->K = (float*)malloc(row_a * row_c * sizeof(float));
mpc_kalman_gain(iterations, sampleTime_kf, mpc->Adkf, mpc->Cdkf, qw, rv, mpc->K, row_a, row_c);

#### Controllability matrix
The controllability matrix Φ in Re^{ (N times nz) times nx } is a large matrix that holds bar C and bar A .
##### Mathematics:
 This is the controllability matrix in Equation 6 where N is the horizon of prediction.
##### MATLAB code:
Φ = left [ matrix{ bar C bar A ## bar C bar A^2 ## bar C bar A^3 ## dotsvert ## bar C bar A^N } right ] Equation 6: Controllability matrix
Phi = PhiMat(Ad, Cd, N);
##### C code:
mpc->Phi = (float*)malloc((N * row_c) * row_a * sizeof(float));
mpc_phi_matrix(mpc->Phi, mpc->Ad, mpc->Cd, row_a, row_c, N);
#### Lower triangular toeplitz of extended observability matrix
The lower triangular toeplitz of extended observability matrix Γ in Re^{ (N times nz) times (N times nu) } is a large matrix that holds H = bar C bar A^N bar B .
##### Mathematics:
The lower triangular toeplitz of extended observability matrix can be seen in Equation 7.
##### MATLAB code:
Γ = left [ matrix{ H_1 # 0 # 0 # dotsaxis # 0 ## H_2 # H_1 # 0 # dotsaxis # 0 ## H_3 # H_2 # H_1 # dotsaxis # 0 ## dotsvert # dotsvert # dotsvert # dotsdown # dotsvert ## H_N # H_{N-1} # H_{N-2} # dotsaxis # H_1 } right ] Equation 7: Lower triangular toeplitz of extended observability matrix
Gamma = GammaMat(Ad, Bd, Cd, N);
##### C code:
float* Gamma = (float*)malloc((N * row_c) * (N * column_b) * sizeof(float));
mpc_gamma_matrix(Gamma, mpc->Phi, mpc->Bd, mpc->Cd, row_a, row_c, column_b, N);

#### Weight matrix
The weight matrix Q_Z in Re^{ (N times nz) times (N times nz) } holds the scalar matrix Q_z in Re^{ nz times nz } . The weight matrix made for determine the weights of the MPC. Small weights will give poor performance. Large weights will give too strong outputs.
##### Mathematics:
The weight matrix can be seen in Equation 8.
##### MATLAB code:
Q_Z = left [ matrix{ Q_z # 0 # dotsaxis # 0 ## 0 # Q_z # dotsaxis # 0 ## dotsvert # dotsvert # dotsdown # dotsvert ## 0 # 0 # dotsaxis # Q_z } right ] Equation 8: Weight matrix
QZ = QZMat(Qz, N, nz);
##### C code:
float* QZ = (float*)malloc((N * row_c) * (N * row_c) * sizeof(float));
mpc_QZ_matrix(QZ, qz, row_c, N);
#### Regularization matrix
The regularization matrix H_S in Re^{(N times nu) times (N times nu)} holds the scalar matrix S in Re^{ nu times nu } . The regularization matrix giving a smoother input signals U from of the MPC. Small values will give coarse and fast performance. Large values will give too smooth and slow performance.
##### Mathematics:
The regularization value and its values can be seen in Equation 9.
##### MATLAB code:
H_S = left [ matrix{ 2S # -S # 0 # 0 # 0 ## -S # 2S # -S # 0 # 0 ## 0 # dotsdown # dotsdown # dotsdown # 0 ## 0 # 0 # -S # 2S # -S ## 0 # 0 # 0 # -S # S} right ] Equation 9: Regularization matrix
S = SMat(s, nu);
HS = HSMat(S, N, nu);
##### C code:
float* S = (float*)malloc(column_b * column_b * sizeof(float));
mpc_S_matrix(S, s, column_b);
float* HS = (float*)malloc((N * column_b) * (N * column_b) * sizeof(float));
mpc_HS_matrix(HS, S, column_b, N);
#### QP solver matrix
The QP solver matrix H in Re^{(N times nu) times (N times nu)} is a matrix for the Quadratic Programming solver.
##### Mathematics:
The QP solver matrix can be seen in Equation 10.

H = Γ^T times Q_Z Γ + H_S Equation 10: The QP solver matrix
##### MATLAB code:
H = HMat(Gamma, QZ, HS);
##### C code:
float* H = (float*)malloc((N * column_b) * (N * column_b) * sizeof(float));
mpc_H_matrix(H, Gamma, QZ, HS, row_c, column_b, N);
#### Lower triangular toeplitz of extended observability matrix of disturbance
The lower triangular toeplitz of extended observability matrix of disturbance Γ_d in Re^{ (N times nz) times (N times nu) } is a large matrix that holds H_d = bar C bar A^N bar E .
##### Mathematics:
The lower triangular toeplitz of extended observability matrix can be seen in Equation 11.
##### MATLAB code:
Γ_d = left [ matrix{ H_{1,d} # 0 # 0 # dotsaxis # 0 ## H_{2,d} # H_{1,d} # 0 # dotsaxis # 0 ## H_{3,d} # H_{2,d} # H_{1,d} # dotsaxis # 0 ## dotsvert # dotsvert # dotsvert # dotsdown # dotsvert ## H_{N,d} # H_{N-1, d} # H_{N-2, d} # dotsaxis # H_{1,d} } right ] Equation 11: Lower triangular toeplitz of extended observability matrix of disturbances
Gammad = GammaMat(Ad, Ed, Cd, N);
##### C code:
float* Gammad = (float*)malloc((N * row_c) * (N * column_e) * sizeof(float));
mpc_gamma_matrix(Gammad, mpc->Phi, mpc->Ed, mpc->Cd, row_a, row_c, column_e, N);
#### QP solver gradient matrices
In order to create the gradient of the QP solver. One must first create its matrices M_{ x_0 } in Re^{ (N times nu) times nx } , M_{ u_{-1} } in Re^{ (N times nu) times nu } , M_{R} in Re^{ (N times nu) times nz } and M_{D} in Re^{ (N times nu) times nd } .
##### Mathematics:

alignl M_{x_0} = Γ times Q_Z times Φ newline alignl M_{ u_{-1} } = S newline alignl M_R = Γ times Q_Z newline alignl M_D = Γ times Q_Z Γ_d Equation 12: QP solver gradient matrices
##### MATLAB code:
Mx0 = Mx0Mat(Gamma, QZ, Phi);
Mum1 = Mum1Mat(N, nu, S);
MR = MRMat(Gamma, QZ);
MD = MDMat(Gamma, QZ, Gammad);
##### C code:
mpc->Mx0 = (float*)malloc((N * column_b) * row_a * sizeof(float));
mpc_Mx0_matrix(mpc->Mx0, Gamma, QZ, mpc->Phi, row_a, row_c, column_b, N);
mpc->Mum1 = (float*)malloc((N * column_b) * column_b * sizeof(float));
mpc_Mum1_matrix(mpc->Mum1, S, column_b, N);
mpc->MR = (float*)malloc((N * column_b) * (N * row_c) * sizeof(float));
mpc_MR_matrix(mpc->MR, Gamma, QZ, row_c, column_b, N);
mpc->MD = (float*)malloc((N * column_b) * (N * column_e) * sizeof(float));
mpc_MD_matrix(mpc->MD, Gamma, mpc->Gammad, QZ, row_c, column_b, column_e, N);
#### Rate of movement matrix
The rate of movement matrix Λ in Re^{ ((N-1) times nu ) times (N times nu) } holds the identity matrix I in Re^{ nu times nu } . The rate of movement matrix controls how fast the input U can change from the MPC.
##### Mathematics:
The rate of movement matrix can be seen in Equation 13.
##### MATLAB code:
Λ = left [ matrix{ -I # I # 0 # 0 # 0 ## 0 # -I # I # 0 # 0 ## 0 # 0 # dotsdown # dotsdown # 0 ## 0 # 0 # 0 # -I # I} right ] Equation 13: Rate of movement matrix
Lambda = LambdaMat(N, nu);
##### C code:
float* Lambda = (float*)malloc(((N - 1) * column_b) * (N * column_b) * sizeof(float));
mpc_Lambda_matrix(Lambda, column_b, N);
#### Slack variables
The slack variable matrix bar S_ Ψ in Re^{ (N times nu) times (N times nu) } holds the scalar matrix S_Ψ in Re^{ nu times nu } and the slack variable vector bar s_ Ψ in Re^{N times nu} holds the vector s_ Ψ in Re^{ nu } . The slack variables increase the guarantee for the QP solver to find a feasible solution of U . The vector s_Ψ in Re shares the same value as the scalar matrix S_Ψ in Re^{ nu times nu } .
##### Mathematics:
The slack variable matrix and vector can be seen in Equation 14 and Equation 15.
##### MATLAB code:
bar S_Ψ = left [ matrix{ S_Ψ # 0 # dotsaxis # 0 ## 0 # S_Ψ # dotsaxis # 0 ## dotsvert # dotsvert # dotsdown # dotsvert ## 0 # 0 # dotsaxis # S_Ψ } right ] Equation 14: Slack variable matrix
bar s_Ψ = left [ matrix{ s_Ψ ## s_Ψ ## dotsvert ## s_Ψ } right ] Equation 15: Slack variable vector
barSpsi = barSpsiMat(Spsi, N, nu);
barspsi = barspsiVec(spsi, N, nu);
##### C code:
float* barSpsi = (float*)malloc((N * column_b) * (N * column_b) * sizeof(float));
mpc_barSpsi_matrix(barSpsi, Spsi_spsi, column_b, N);
mpc->barspsi = (float*)malloc(N * column_b * sizeof(float));
mpc_barspsi_vector(mpc->barspsi, Spsi_spsi, column_b, N);
#### QP solver matrix with slack variables
Here we create another QP solver matrix bar H_S in Re^{ (2 times N times nu) times (2 times N times nu) } that contains slack variables.
##### Mathematics:
The QP solver matrix with containing slack variables can be seen in Equation 16.

bar H_S = left [ matrix{H_S # 0 ## 0 # bar S_Ψ} right ] Equation 16: QP solver matrix with slack variables
##### MATLAB code:
barH = barHMat(H, barSpsi, N, nu);
##### C code:
mpc->barH = (float*)malloc((2 * N * column_b) * (2 * N * column_b) * sizeof(float));
mpc_barH_matrix(mpc->barH, H, barSpsi, column_b, N);
#### Inequality constraints
The reason why MPC is used, it’s because its constraints. Enabling the limitation to the control input signal U . This could also be done with signal saturation, with loss of stability guarantees. Therefore inequality constraints AA in Re^{ ((N - 1) times nu + 2 times N times nz) times (2 times N times nu) } can be used to keep the stability guarantees.
##### Mathematics:
The inequality constraints matrix can be seen in Equation 17.

AA = left [ matrix{ Λ # 0 ## Γ # -I ## Γ # I} right ] Equation 17: Inequality constraints
##### MATLAB code:
AA = AAMat(Lambda, Gamma, N, nu, nz);
##### C code:
mpc->AA = (float*)malloc(((N - 1) * column_b + 2 * N * row_c) * (2 * N * column_b) * sizeof(float));
mpc_AA_matrix(mpc->AA, Lambda, Gamma, row_c, column_b, N);
#### Holder arrays
It’s important in C programming language to declare initial arrays for the optimization function. They are only used for store data such as the state vector, integral value and user settings such as constraints.
##### Mathematics:
No mathematics provided here.
##### MATLAB code:
No MATLAB code provided here.
##### C code:
mpc->eta = (float*)malloc(row_c * sizeof(float));
memset(mpc->eta, 0, row_c * sizeof(float));
mpc->x = (float*)malloc(row_a * sizeof(float));
memset(mpc->x, 0, row_a * sizeof(float));
mpc->deltaumin = (float*)malloc(column_b * sizeof(float));
mpc->deltaumax = (float*)malloc(column_b * sizeof(float));
mpc->umin = (float*)malloc(column_b * sizeof(float));
mpc->umax = (float*)malloc(column_b * sizeof(float));
mpc->is_initlized = true;
### mpc_set_constraints
#### Input constraints
After initialization of the matrices for the MPC are done. Then the need of setting the values for the constraints are mandatory. The constraints that are going to be set are the minimum input signal limit u_min in Re^{ nu } , the maximum input signal limit u_max in Re^{ nu } , the minimum output signal limit Z_min in Re^{ N times nz } , the maximum output signal limit Z_max in Re^{ N times nz } , the minimum rate of change input limit ΔU_min in Re^{(N-1) times nu } and the maximum rate of change input limit ΔU_max in Re^{(N - 1) times nu } .
##### Mathematics:

alignl Z_min = left [ matrix{z_{min} ## z_{min} ## dotsvert ## z_{min}} right ] newline alignl Z_max = left [ matrix{z_{max} ## z_{max} ## dotsvert ## z_{min}} right ] newline alignl ΔU_min = left [ matrix{Δu_{min} ## Δu_{min} ## dotsvert ## Δu_{min}} right ] newline alignl Δu_max = left [ matrix{Δu_{max} ## Δu_{max} ## dotsvert ## Δu_{max}} right ] newline Equation 18: Constraints
##### MATLAB code:
No MATLAB code provided here.
##### C code:
mpc_set_input_constraints(mpc, umin, umax);
mpc_set_output_constraints(mpc, zmin, zmax);
mpc_set_input_change_constraints(mpc, deltaumin, deltaumax);
### mpc_optimize
#### Integral action
This MPC algorithm has integral action included. The integral action is an addition to the reference vector. The integral is summation of the error of the trajectory.
##### Mathematics:
alignl Ψ = r - y newline alignl η = η + α times Ψ newline alignl η = left lbrace matrix{antiwindup times σ(η), if abs{η} > antiwindup ## η} right rbrace
##### MATLAB code:
psi = r - y;
eta = eta + alpha*psi;
if(abs(eta) > antiwindup)
   eta = sign(eta)*antiwindup;
end
##### C code:
mpc_eta_vector(mpc->eta, r, y, mpc->alpha, integral_active, row_c);
mpc_antiwindup_vector(mpc->eta, mpc->antiwindup, row_c);
#### Reference vector
The reference vector R in Re^{ N times nz } holds the vector r in Re^nz . The reference vector is the trajectory vector where the user want the output of the plant to follow.
##### Mathematics:
The reference vector can be seen in Equation 19.
##### MATLAB code:
R = left [ matrix{ r_1 ## r_2 ## r_3 ## dotsvert ## r_N } right ] Equation 19: Reference vector
R = RVec(r, N);
##### C code:
float* R = (float*)malloc(N * row_c * sizeof(float));
mpc_vector(R, r, row_c, N);
#### Disturbance vector
The disturbance vector D in Re^{ N times nd } holds the vector d in Re^nd . The disturbance vector is the measurement vector which affects the output of the plant. In other words, the disturbance vector is a measurement signal from a sensor attached onto the plant.
##### Mathematics:
The reference vector can be seen in Equation 20.
##### MATLAB code:
D = left [ matrix{ d_1 ## d_2 ## d_3 ## dotsvert ## d_N } right ] Equation 20: Reference vector
D = DVec(d, N);
##### C code:
float* D = (float*)malloc(N * column_e * sizeof(float));
mpc_vector(D, d, column_e, N);
#### QP gradient vector
The QP algorithm requires the gradient vector g in Re^{ N times nu } .
##### Mathematics:
The gradient vector can be seen in Equation 21.

g = M_{ x_0 } times x M_R times (R + η) + M_D times D + M_{ u_{m-1 }} times u_{ -1 } Equation 21: Gradient vector
##### MATLAB code:
um1 = u;
Ri = repmat(eta, N, 1);
g = gVec(Mx0, x, MR, R + Ri, MD, D, Mum1, um1);
##### C code:
float* um1 = (float*)malloc(column_b * sizeof(float));
memcpy(um1, u, column_b * sizeof(float));
float* g = (float*)malloc(N * column_b * sizeof(float));
mpc_g_vector(g, mpc->Mx0, mpc->x, mpc->MR, R, mpc->eta, mpc->MD, D, mpc->Mum1, um1, row_a, row_c, column_b, column_e, N);
#### Constraints on inputs
The constraints on input U are U_min in Re^{ N times nu } and U_max in Re^{ N times nu } .
##### Mathematics:
The constraints on input U can be seen in Equation 22.

alignl U_min = left [ matrix{max(u_min, Δu_min + u_{-1}) ## u_min ## u_min ## dotsvert ## u_min} right ], U_max = left [ matrix{min(u_max, Δu_max + u_{-1}) ## u_max ## u_max ## dotsvert ## u_max} right ] Equation 22: Constraints on input U
##### MATLAB code:
Umin = UminVec(umin, deltaumin, um1, N, nu);
Umax = UmaxVec(umax, deltaumax, um1, N, nu);
##### C code:
float* Umin = (float*)malloc(N * column_b * sizeof(float));
float* Umax = (float*)malloc(N * column_b * sizeof(float));
mpc_Umin_vector(Umin, mpc->umin, mpc->deltaumin, um1, N, column_b);
mpc_Umax_vector(Umax, mpc->umax, mpc->deltaumax, um1, N, column_b);
#### Constraints on outputs
The constraints on output Z are bar Z_min in Re^{ N times nz } and bar Z_max in Re^{ N times nz } .
##### Mathematics:
The constraints on output Z can be seen in Equation 23.

alignl bar Z_min = Z_min + Φ times x_0 + Γ_d times D newline alignl bar Z_max = Z_min - Φ times x_0 - Γ_d times D Equation 23: Constraints on output Z
##### MATLAB code:
barZmin = barZminVec(Zmin, Phi, x, Gammad, D);
barZmax = barZmaxVec(Zmax, Phi, x, Gammad, D);
##### C code:
float* barZmin = (float*)malloc(N * row_c * sizeof(float));
float* barZmax = (float*)malloc(N * row_c * sizeof(float));
mpc_barZmin_vector(barZmin, mpc->Zmin, mpc->Phi, mpc->x, mpc->Gammad, D, row_a, row_c, column_b, column_e, N);
mpc_barZmax_vector(barZmax, mpc->Zmax, mpc->Phi, mpc->x, mpc->Gammad, D, row_a, row_c, column_b, column_e, N);
#### Gradient vector with soft output constraints
The gradient vector g with soft output constraints is called bar g in Re^{N times nu + N times nu} .
##### Mathematics:
The gradient vector bar g can be seen in Equation 24.

bar g = left [ matrix{ g ## bar s_Ψ } right ] Equation 24: The gradient vector bar g
##### MATLAB code:
barg = bargVec(g, barspsi);
##### C code:
float* barg = (float*)malloc((N * column_b + column_b * N) * sizeof(float));
mpc_barg_vector(barg, g, mpc->barspsi, column_b, N);
#### Modified constraints on input
The modified constraints on input U is called bar U_min in Re^{N times nu + N} and bar U_max in Re^{N times nu + N} .
##### Mathematics:
The modified constraints bar U_min in Re^{N times nu + N} and bar U_max in Re^{N times nu + N} can be seen in Equation 25.

alignl bar U_min = left [ matrix{ U_min ## 0} right ] newline alignl bar U_max = left [ matrix{ U_max ## infinity } right ] Equation 25: The modified constraints on inputs
##### MATLAB code:
barUmin = barUminVec(Umin, N);
barUmax = barUmaxVec(Umax, infinity, N);
UI = eye(N * nu + N, 2 * N * nu);
##### C code:
float* barUmin = (float*)malloc((N * column_b + N) * sizeof(float));
float* barUmax = (float*)malloc((N * column_b + N) * sizeof(float));
mpc_barUmin_vector(barUmin, Umin, column_b, N);
mpc_barUmax_vector(barUmax, Umax, column_b, N);
#### Quadratic programming
The quadratic programming is applied with all the inequality constraints: b_min in Re^{(N - 1) times nu + N times nz + N times nz} , b_max in Re^{(N - 1) times nu + N times nz + N times nz} , a_qp in Re^{(2 times ((N - 1) times nu + 2 times N times nz) + 2 times (N times nu + N)) times (2 times N times nu)} and b_qp in Re^{2 times (N times nu + N) + 2 times ((N - 1) times nu + N times nz + N times nz)} .
##### Mathematics:
The inequality constraints constraints of the quadratic programming can be seen in Equation 26.

alignl b_min = left [ matrix{ ΔU_min ## -infinity ## bar Z_min} right ], b_max = left [ matrix{ ΔU_max ## Z_max ## infinity } right ] , a_qp = left [ matrix{ UI ## AA ## -UI ## -AA} right ], b_qp = left [ matrix{bar U_max ## bar b_max ## bar -U_min ## b_min} right ] Equation 26: The inequality constraints for the QP
The objective function can be see in Equation 27.

alignl {min} underbrace {bar U} : Φ = 1 over 2 times bar U^T times bar H times bar U + bar g^T times bar U newline alignl s.t: b_min <= bar U <= b_max newline alignl s.t: a_qp times bar U <= b_qp Equation 27: The objective function of QP
##### MATLAB code:
bmin = bminVec(deltaUmin, barZmin, infinity, N, nz);
bmax = bmaxVec(deltaUmax, barZmax, infinity, N, nz);
aqp = [UI; AA; -UI; -AA];
bqp = [barUmax; bmax; -barUmin; -bmin];
##### C code:
float* bmin = (float*)malloc(((N - 1) * column_b + N * row_c + N * row_c) * sizeof(float));
float* bmax = (float*)malloc(((N - 1) * column_b + N * row_c + N * row_c) * sizeof(float));
mpc_bmax_vector(bmax, mpc->deltaUmax, barZmax, column_b, row_c, N);
mpc_bmin_vector(bmin, mpc->deltaUmin, barZmin, column_b, row_c, N);
float* aqp = (float*)malloc((2 * ((N - 1) * column_b + 2 * N * row_c) + 2 * (N * column_b + N)) * (2 * N * column_b) * sizeof(float));
float* bqp = (float*)malloc((2 * (N * column_b + N) + 2 * ((N - 1) * column_b + N * row_c + N * row_c)) * sizeof(float));
mpc_aqp_matrix(aqp, mpc->AA, column_b, row_c, N);
mpc_bqp_vector(bqp, barUmin, barUmax, bmin, bmax, column_b, row_c, N);
float* U = (float*)malloc(2 * N * column_b * sizeof(float));
const STATUS_CODES status = quadprogslim(mpc->barH, barg, aqp, bqp, NULL, NULL, U, 2 * ((N - 1) * column_b + 2 * N * row_c) + 2 * (N * column_b + N), 0, 2 * N * column_b, false);
memcpy(u, U, column_b * sizeof(float));